## Slide 1: clues
Energy is only speed dependant => no height consideration
MyEnergy & EnemyEnergy : comparison, bleeding, growing => isBleedingEnergy(speed, G)
History: Answer the question : Has he been losing energy for a long time ? => to prevent the AI to avoid all the situations that bleed energy, whereas it is sometimes necessary.
Energy danger: take into account the previous clues to say if the situation is dangerous
Decide what parameter, between G and Speed should be protected, concerning the energy issue
TO DO : specify these functions, and then propose a class diagram

## Slide 2: 1 – both energies
Compare energies  Compare speeds
Energy bleeding or growing ?
If speed <= 440
If speed > 440
Border : G = α0V+ β0
α0 = 5/270, β0 = -1.1481
Border : G0 = 7
Below the border : energy is growing Above the border : energy is bleeding
Assumption : 0.9 Mach = 440 knots, 0.68 Mach = 330 knots
‘Energy is growing’ and ‘Energy is bleeding’ should more precise => how much ?
=> (G,V)  resulting acceleration
G = αV+ β (α0, β0, G0) => no gain (α1, β1, G1) => -200, G1 = 8 (α2, β2, G2) => -400, , G2 = 8.5 (α3, β3) => -600 (α4, β4) => -800 (α5, β5) => -1000
Simplification: Vlimit = 440 for every α αi = α0 for every I G <= 9

## Slide 3: 2 - History
The goal is to know, how long the aircraft has been bleeding energy. If this situation is new, it will prevent the AI to interpret this as a danger.
History > 0 E increasing History < 0  E decreasing History = 0  sense of variation has changed
Test Energy
If bleeding
If gaining
Update history(bleeding)
If history > 0
If history <= 0
History = 0
History -= period
Update history(gaining)
If history < 0
If history >= 0
History = 0
History += period
Test Instruction

## Slide 4: 3 – Energy Danger
ΔE = My Energy – Enemy Energy
ΔE
ΔE > 0
ΔE < 0
Energy advantage
IF MyE.isGrowing() OR IF !MyE.isGrowing() AND !EE.isGrowing()
No danger
IF !MyE.isGrowing() AND EE.isGrowing()
Potential danger
Energy disadvantage
IF MyE.isGrowing() AND !EE.isGrowing()
No danger
IF !MyE.isGrowing() OR MyE.isGrowing() AND EE.isGrowing()
Potential danger
History is not taken into account, useless ?
Do we have access to how Enemy energy is increasing or decreasing. If yes, maybe it’s better to use it than the fact that it is growing or not.

## Slide 5: 4 – To be saved
If there is an energy danger, G or V or both should be saved
The point is to calculate the distance between the current point (G,V) to the border (no gain or waste of energy).
G_distance
If V > 440
G_distance = (G – 7) / (Gmax –Gmin)
G_distance = (G – α0V+ β0) / (Gmax –Gmin)
If V <= 440
V_distance
If G > 7
V_distance = not defined
V_distance = (V – (G - β0) / α0) / (Vmax –Vmin)
If G <= 7
G_distance * V_distance >= 0
G_distance * V_distance < 0
To be saved
IF G_distance < V_distance
IF G_distance > V_distance
Save G
Save V
IF G_distance > 0
IF V_distance > 0
Save G
Save V
V_distance not defined
Save G
AI
Energy Recognizer